## Slide 1
TEAM KNOWLEDGE SHARING
CAN Routine Message
over SOME/IP
End-to-end data flow through the AUTOSAR Classic stack
CAN Rx
›
COM callout
›
OS task
›
SOME/IP
›
Ethernet
Application
RTE
Communication Services
ECU Abstraction
MCAL / Drivers
Bus
Rx
Tx
Notes: Goal of this session: give the team a shared mental model of how a routine CAN message is received and re-published as a SOME/IP message over Ethernet, and which AUTOSAR module owns each step.

## Slide 2
End-to-end flow across the AUTOSAR stack
Rx — CAN reception
Tx — SOME/IP transmission
Application
RTE
Communication
Services
ECU Abstraction
MCAL / Drivers
Bus / Network
CAN Bus
CanDrv
1
CanIf
2
PduR
3
Com
4
CAN Rx interrupt
PduCallout copies the data
SWC runnable / OS extended task
5
RTE
6
SetEvent
WaitEvent → send
SomeIpXf
7
LdCom
8
PduR
9
SoAd
10
EthIf
11
EthDrv
12
Ethernet
adds 8-byte SOME/IP header
adds Message ID + Length
Notes: One picture for the whole feature. Left column = reception, right column = transmission. The two halves meet in the Application layer: the COM PduCallout copies the payload and sets an OS event; the extended task wakes up and drives the SOME/IP transmission down the Ethernet stack. Note that the received data never travels through the RTE - it is copied inside the callout.

## Slide 3
Rx path — CAN bus to COM callout
Steps 1–4 · runs in CAN receive context
CAN Bus
CanDrv
1
Rx interrupt
CanIf
2
HRH → Rx PDU
PduR
3
routing path
Com
4
PduCallout
CAN Rx interrupt context
1
Trigger
CAN frame arrives → Rx interrupt
2
Copy
PduCallout copies the signal data
into the SOME/IP transmit buffer
3
Hand-off
SetEvent wakes the sending task —
no blocking work inside the callout
Notes: The whole receive chain is the standard AUTOSAR path. The only project-specific part is the COM PduCallout: it is our hook to grab the freshly received data and pass it on. Keep the callout short - copy and signal only, never send from here.

## Slide 4
Tx path — OS task to Ethernet
Steps 5–12 · runs in the extended OS task context
OS task
5
WaitEvent
RTE
6
SomeIpXf
7
+ 8-byte header
LdCom
8
PduR
9
SoAd
10
+ Message ID, Length
EthIf
11
EthDrv
12
on the wire
How the frame grows
after RTE
CAN signal data
after SomeIpXf
SOME/IP header
8 B
CAN signal data
after SoAd
Message ID
+ Length · 8 B
SOME/IP header
8 B
CAN signal data
16-byte SOME/IP header in total — 8 B added by the transformer, 8 B by SoAd
Notes: Transmission runs entirely in the extended task, so it never blocks the CAN interrupt. SomeIpXf serializes the data and adds its 8 header bytes; SoAd prepends the Message ID (Service ID + Method/Event ID) and the Length field. EthIf and EthDrv then put the frame on the wire.